## Slide 1: FreeRtos Course (Day 1)
By: Mahmoud Elsheemy

## Slide 2: RTOS vs Bare-Metal Architecture

## Slide 3: Bare-Metal Architecture (super loop)
Super loop contains the program flow:
  Input
  Processing
  Output
  Delay
Any system can be designed by a super loop
System is not deterministic
Hard to maintain
Hard to design a whole system inside the super loop

## Slide 4: Bare-Metal Architecture Example
check_brakes()
Measure_speed()
check_oil()
check_doorlock()

## Slide 5: Real-Time Operating System (RTOS)
Break down the main program into set of tasks.
Each task has a periodicity and a priority.
There is a scheduler that switches between the tasks.
Deterministic.
Easy to design (modular design) , easy to maintain.
It’s the programmer task to have a good design before implementation.

## Slide 6: RTOS example
Scheduler switch between tasks
Each task has a priority and a periodicity
Scheduler
Check_brakes()
Check_oil()
Check_radio()
Check_door()

## Slide 7: Let’s Implement RTOS in our code!

## Slide 8: Introduction to FreeRTOS
Market leading cross platform RTOS kernel for microcontrollers and small microprocessors
Simple API
FreeRTOS offer RTOS implementation for any microcontroller
Download your microcontroller FreeRTOS files from here https://www.freertos.org/a00104.html

## Slide 9: FreeRTOS in arduino